## Slide 1
POWERPOOL
Neighbourhood-Scale Residential Load Flexibility for Distribution Grid Reliability
Yuva Yodha Energy Tech Hackathon 2026 • Challenge 03: Grid Reliability Simulated 170 kW Low-Voltage Distribution Feeder Architecture
Notes: Welcome judges. PowerPool addresses Challenge 03 by coordinating residential load flexibility to support grid reliability. We model a simulated 170 kW low-voltage distribution transformer facing evening solar drop-off and peak residential demand surges.

## Slide 2
POWERPOOL • YUVA YODHA HACKATHON 2026
The Grid Reliability Challenge: Distribution Transformer Overload
1. The Evening Solar Cliff
Solar generation drops to 0 kW between 17:30 and 18:30.
Simultaneous surge in cooking, water heating, cooling, and vehicle charging.
Creates a sharp net-demand ramp on the local substation.
2. Transformer Thermal Strain
Assumed Simulated Feeder Capacity: 170.0 kW.
Typical Baseline Peak: ~196.00 kW (approx 26 kW overload).
Heatwave Extreme Peak: 388.91 kW (severe 218 kW overload).
Risk of accelerated thermal aging, insulation degradation, and tripping.
3. The Need for Load Flexibility
Traditional remedies: Costly transformer upgrades or diesel peakers.
Consumer impact: Unscheduled supply interruptions during peak hours.
Opportunity: Shift flexible household cycles into midday solar hours.
Notes: Low-voltage distribution transformers face peak thermal stress when solar generation collapses at sunset just as residential evening demand surges. On our simulated 170 kW feeder, unmanaged demand exceeds capacity, highlighting the need for coordinated load flexibility.

## Slide 3
POWERPOOL • YUVA YODHA HACKATHON 2026
System Architecture: End-to-End Predictive Flexibility
Data & Forecast Engine
30-day 15-minute load history telemetry (288,000 intervals).
Open-Meteo weather integration (temperature, cloud cover, irradiance).
150-tree LightGBM predictive model.
Transparent dual-horizon accuracy assessment.
Two-Stage Optimization Engine
Stage 1: Capacity-aware voluntary shift optimizer.
Enforces appliance time windows & exact energy conservation.
Destination-block checks prevent midday rebound peaks.
Stage 2: Mathematical simulation of aggregate emergency curtailment.
DISCOM & Resident Interfaces
Streamlit Command Center with live ML inference toggle.
Automated Feasibility Status badge & bottleneck diagnosis.
Resident Portal with English, Hindi, and Telugu nudges.
Estimated Time-of-Day tariff savings calculation & rewards.
Notes: PowerPool integrates three components: predictive demand forecasting with LightGBM, a two-stage optimization engine, and a multi-lingual resident portal, backed by a FastAPI service and SQLite database.

## Slide 4
POWERPOOL • YUVA YODHA HACKATHON 2026
AI Demand Forecasting: Evaluating Two Distinct Operational Horizons
Recursive Day-Ahead Planning (24-Hour Horizon)
Operational Scope: Day-ahead scheduling (00:00–23:45).
Evaluation: True recursive inference (zero intra-day observations).
Key Features: lag_96, lag_192, calendar variables, forecast weather.
LightGBM MAE: 2.42 kW (RMSE: 3.23 kW, MAPE: 3.24%).
Seasonal Baseline MAE: 2.84 kW (RMSE: 4.24 kW, MAPE: 3.21%).
Error Reduction: ~14.8% improvement over seasonal baseline.
Peak Forecast Error: 3.47 kW vs 10.01 kW for seasonal baseline.
Intraday Rolling Dispatch (15-Minute Horizon)
Operational Scope: Real-time grid balancing & intraday re-dispatch.
Evaluation: 1-step-ahead rolling inference using recent observed demand.
Features: Incorporates recently observed lag_1 & lag_4 demand.
LightGBM MAE: 2.10 kW (RMSE: 2.90 kW, MAPE: 2.77%).
Seasonal Baseline MAE: 2.84 kW.
Error Reduction: 26.1% lower MAE under rolling telemetry updates.
Critical Distinction: Rolling performance requires recent telemetry and is not day-ahead planning.
Notes: We evaluate our forecasting model under two distinct operational conditions. For 24-hour day-ahead planning with zero future data, recursive LightGBM achieves a 2.42 kW MAE, an approximately 14.8% error reduction over the seasonal baseline, with a peak forecast error of 3.47 kW versus 10.01 kW. For 15-minute rolling updates with incoming telemetry, the one-step MAE is 2.10 kW. These represent separate forecasting conditions.

## Slide 5
POWERPOOL • YUVA YODHA HACKATHON 2026
Stage 1: Capacity-Aware Voluntary Load Shifting
Mathematical Principles & Constraints
1. Operating Window Constraints:
• Every shift strictly respects resident [earliest_slot, latest_slot].
• 0 constraint violations across registered devices.
2. Exact Energy Conservation:
• Energy removed from peak equals energy added to solar hours.
• Net energy delta is mathematically zero (0.000000 kWh).
3. Rebound Peak Protection:
• Destination-block load checks prevent creating new midday peaks.
Primary Live Application Results (80 Households)
Scope: Registered 80-household community (275 appliances).
Baseline Evening Peak: ~196.00 kW (exceeds 170 kW rating).
Stage 1 Optimized Peak: 155.50 kW.
Peak Reduction: -40.50 kW (-20.7%).
Scheduled Shifted Energy: 121.50 kWh across 27 scheduled shifts.
Realized Shifted Energy: ~79.0 kWh modeled at 65% compliance.
Remaining Overload: 0.00 kW (155.5 kW <= 170 kW → Status: FEASIBLE).
Notes: On our primary live application with 80 registered households, Stage 1 optimization schedules 27 shifts moving 121.50 kWh into solar hours, resulting in approximately 79.0 kWh realized under our 65% compliance model. Peak demand is reduced from 196.0 kW to 155.5 kW—a 20.7% reduction that brings the simulated feeder within its 170 kW threshold without creating rebound peaks.

## Slide 6
POWERPOOL • YUVA YODHA HACKATHON 2026
Grid Reliability Assessment: Stage 2 Modeled Emergency Interventions
Modeled Interventions (Analytic Capacity Cap)
Mathematical simulation of aggregate emergency curtailment.
Models potential utility interventions: EV throttle & thermostat adjustments.
Modeled maximum curtailment parameter: 120.0 kW.
Evaluates grid feasibility limits when voluntary shifting is insufficient.
Clear Boundary: An analytic simulation, not physical hardware control.
Extreme Heatwave Stress-Test Findings
Context: High-stress feeder profile under extreme 42°C heatwave.
Baseline Peak: 388.91 kW → Stage 1 Peak: 302.52 kW.
Overload Remaining Above 170 kW: 132.52 kW.
Maximum Modeled Emergency Curtailment: 120.00 kW.
Simulated Peak after Stage 2: 182.52 kW.
Residual Overload: 12.52 kW across 3 peak intervals.
Key Insight: Transparently exposes physical deficits where voluntary shifting and modeled reserves cannot fully eliminate overload.
Notes: Stage 2 is an analytic emergency curtailment model with an assumed 120 kW maximum, not a physical hardware control system. In our extreme heatwave stress test, voluntary shifts leave a 132.52 kW overload. Even with 120 kW of modeled emergency curtailment, a 12.52 kW residual overload remains. PowerPool reports these physical boundaries honestly.

## Slide 7
POWERPOOL • YUVA YODHA HACKATHON 2026
Resident Engagement: Multi-Lingual Nudges & ToD Economics
Personalized Multi-Lingual Nudges
Natively supports English, Hindi, and Telugu.
Deterministic templates tailored to resident language preference.
Device-specific guidance: Washing machine, Geyser, Water pump, EV.
Actionable messaging: 'Shift cycle to 13:00 to utilize solar generation.'
Time-of-Day Tariff Differential Savings
Modeled Indian DISCOM Time-of-Day Tariff Structure:
• Peak Tariff (18:00–22:00): Rs 9.00 / kWh.
• Solar Off-Peak Tariff (10:00–16:00): Rs 6.00 / kWh.
• Tariff Differential: Rs 3.00 / kWh.
Formula: Estimated Bill Savings = Shifted kWh × Rs 3.00 / kWh.
Gamified Points: 10 points awarded per shifted kWh.
Clarification: Estimated savings under modeled tariff, not cash guarantees.
Notes: Resident participation is driven by transparent incentives. We deliver nudges in English, Hindi, or Telugu. Estimated bill savings are calculated using a modeled Rs 3.00/kWh Time-of-Day tariff differential between peak and solar off-peak rates. Nudge acceptances award points on the community leaderboard.

## Slide 8
POWERPOOL • YUVA YODHA HACKATHON 2026
Dataset Provenance: Clear Separation of Experimental Configurations
1. Live Web Application
Database: data/powerpool.db (primary live demo).
Scale: 80 Households, 275 Appliances.
Baseline Peak: ~196.00 kW → Stage 1: 155.50 kW (-20.7%).
Energy: 121.50 kWh scheduled / ~79.0 kWh realized (65% comp).
Remaining Overload: 0.00 kW (FEASIBLE).
2. High-Stress Feeder Profile
Dataset: 100-HH load_history (288k rows) & generator.
Scale: 100 Households, 597 appliances (148 flexible).
Sunny: 121.50 kWh scheduled / 78.97 kWh realized (65% comp).
Cloudy: 416.25 kWh scheduled / 270.56 kWh realized (65% comp).
Heatwave: 425.75 kWh scheduled / 276.74 kWh realized (65% comp).
Baseline Peaks: 340.32 kW (Sunny) / 388.91 kW (Heatwave).
3. Standalone CLI Demo Runner
Script: scripts/run_demo.py & isolated demo database.
Scale: 100 synthetic Households, 345 appliances.
Baseline Peak: 340.32 kW → Stage 1: 258.89 kW (-23.9%).
Energy: 345.75 kWh scheduled.
Remaining Overload: 88.89 kW (PARTIAL RELIEF).
Notes: We maintain strict provenance across three separate configurations: our live 80-household application, the 100-household profile used for ML training and scenario evaluation (yielding 121.5 kWh scheduled on Sunny, 416.3 kWh on Cloudy, and 425.8 kWh on Heatwave), and our standalone CLI runner. We do not blend metrics across these configurations.

## Slide 9
POWERPOOL • YUVA YODHA HACKATHON 2026
Engineering Rigor: Automated Testing & Database Integrity
Automated Test Suite (197 / 197 Passed)
Executed in 35.07 seconds with zero failures.
Verified Test Coverage:
• ML model loading & 13-feature pipeline integrity.
• Appliance operating window constraint validation.
• Mathematical energy conservation tests.
• Rebound-peak prevention in destination blocks.
• Multi-lingual translation consistency (en/hi/te).
• API contract compatibility & scenario propagation.
Production Database Safety & Integrity
Database File: data/powerpool.db (37,224,448 bytes).
Verified Unchanged during Audit: SHA256 1A352F8813CBA41C...
SQLite PRAGMA integrity_check = ok | Foreign keys: 0 violations.
Row Counts Preserved: load_history (288,000), weather (2,880), appliances (275), households (80), forecast (96).
Isolated test fixtures prevented production database mutations.
Notes: Our test suite of 197 automated tests passed in 35 seconds across all functional modules. The production database maintained structural integrity with zero row modifications during audit testing, confirmed by SQLite integrity checks.

## Slide 10
POWERPOOL • YUVA YODHA HACKATHON 2026
Conclusion & Real-World Deployment Roadmap
Current Status: Tested Prototype for Demonstration
Demonstrated End-to-End Capabilities:
• Recursive day-ahead LightGBM forecasting (~14.8% error reduction).
• Capacity-aware optimization shaving 20.7% peak demand.
• Honest feasibility reporting and residual overload diagnostics.
• Multi-lingual civic engagement with ToD tariff savings.
• Tested prototype ready for live hackathon demonstration.
Roadmap for Real-World Utility Deployment
1. Automated Load Disaggregation: Non-Intrusive Load Monitoring (NILM) on AMI smart meter data.
2. Protocol Integration: OpenADR 2.0b Virtual End Node (VEN) client.
3. Smart EVSE Control: OCPI protocol adapters for direct charging rate modulation.
4. Dynamic Behavioral Compliance: Weather and incentive-sensitive adoption models.
5. Utility SCADA Interfacing: Direct ingestion of substation telemetry.
Notes: PowerPool demonstrates that predictive, coordinated residential load flexibility can effectively mitigate distribution transformer overload. While our current implementation is a software prototype ready for demonstration, we have identified a clear roadmap for real-world utility integration. Thank you!